APES Study Guide

Air Pollution

Mrs. Ashley

Air Pollution (Endangered Global Commons)

Natural Air Pollutants

Volcanoes		sulfur oxides, particulates

Forest Fires		Carbon monoxides, carbon dioxide, Nitrogen oxides, 					particulates

Wind storms		Dust

Living Plants		Hydrocarbons, pollen

Decaying plants	Methane, hydrogen sulfide

Sea			Salt particulates

Major Air Pollutants

Carbon Monoxide	From transportation	     	Causes headache, dizziness, decreased 								tolerance to exercise

Sulfur oxides		Coal fired power plants	Asthma, bronchitis

industry

Nitrogen Oxides	Transportation, Coal fired	lung irritation, bronchitis

Power plants

Particulates		Coal fired power plants	Irritation of respiratory tract, cancer

Industry

Hydrocarbons		Transportation			Unknown

Photochemical

Oxidants		Transportation, coal fired	Respiratory irritation, emphysems

Power plants, industry

Components of fossil fuel

Hydrocarbons	when incompletely burned form: carbon monoxide, unburned hydrocarbons and water

Hydrocarbons when completely burned form: carbon dioxide and water

Contaminants: sulfur---(heated)---Sulfur dioxide and sulfur trioxide

Mineral contaminant---(heated)…Particulates (e.g. lead and mercury)

Nitrogen gas----(heated)…Nitric oxide and nitrogen dioxide

Many of the pollutants react with solar energy and water to produce secondary pollutants, for example sulfur dioxide and water form sulfuric acid.

Photochemical smog-  unburned hydrocarbons and nitrogen oxides from power plants and automobiles react with sunlight to form secondary pollutants: ozone, formaldehyde, PAN.  Ozone erodes rubber, irritates the respiratory system and damages plants.

Temperature inversion

Cleaner air

Bag filter at electric power plants  remove particulates

Cyclone collector particulate removal- used in smaller industry

Electrostatic precipitator removal of particulates at coal fired electric plants

Spray collector, also called a scrubber removes particulates and gases such as sulfur dioxide goes through mist of water and lime.  Nitrogen oxides and carbon dioxide are not removed

Catalytic converter (on cars) transform carbon monoxide and hydrocarbons into water and carbon dioxide

Indoor air pollution

Tobacco smoke (particulates, carbon monoxide, sulfur dioxide, nitrogen dioxide)

From cigarettes, pipe and cigars		Particulates-lung cancer

Carbon monoxide-shortness of breath

Sulfur and carbon dioxide-emphysema 								and chronic bronchitis

Carbon monoxide-heart attack

Radon	(radioactive material found in soil)	Lung cancer

Formaldehyde (New furniture, particle board, plywood, chipboard,  and wood paneling)						lung cancer and nasal cancer

Asbestos (insulation around pipes in old homes, school building and factories)

Lung cancer and build up of fibrous 									tissue in lungs

Ozone depletion

Chlorofluorocarbons (Freon used in refrigerators and air conditioners)

Carbon tetrachloride (cleaning agent)

High altitude jets (less than from chlorofluorocarbons)

Results in increase in ultraviolet radiation—lethal to plants in large doses, inhibits photosynthesis, causes mutations, decline in commercial crops, skin cancer, cataracts

Acid deposition

Lower pH as a result of sulfur reacts with water to form sulfuric acid and nitrogen oxides form nitric acid (wet deposition as rain or fog, dry deposition settles and then later mixes with water

Results in acidification of lakes, killing fish from lower pH and acid rainfall dissolves toxic elements from soil and rocks (aluminum,)  When snow melts in spring acid is damaging to fish eggs, and adult fish as well, affects song birds eggs, amphibians, forest and crop damage weakening trees.  In some instances acid rain may enhance  soil fertility.

Some lakes contain buffers that resist changes in pH.  Thin soiled areas have less buffering capacity.

Greenhouse gases (global climate change)

Carbon dioxide from fossil fuels		coal, oil, natural gas, deforestation

Carbon dioxide from natural sources

Chlorofluorocarbons (CFCs)			foams, aerosols, refrigerants, solvents

Methane (CH4)				wetlands, rice, fossil fuels, livestock

Nitrous oxide (N2O)				Fossil fuels, fertilizers, deforestation

Laws and Protocols

Montreal Protocol

National Acid precipitation Act

National Acid Precipitation Assessment Program (NAPAP)

Kyoto Protocol

Clean Air Act